# 地源热泵

## 简介
地源热泵， Name des Artikels， Name of the article，是指利用浅层地热能为建筑供冷、采暖或制生活热水的热泵装置。[1)]
[1)] 作者姓名，参考文献名称，发表年限，发表地点 - 进一步说明
## 工作原理
冬季： 地源热泵将地热能传递入建筑以为建筑采暖。 Geothermal heat pumps transfer underground heat into buildings to provide heating.
夏季： 地源热泵将热能从建筑传递入地下以为建筑制冷。 Geothermal heat pumps transfer heat from buildings into the ground to provide cooling.
## 分类
1、垂直埋管地源热泵Vertical Closed-Loop
一对底部装配有特殊U型的管道放置在100至400英尺深的孔洞中。 A pair of pipes with a special U-bend assembly at the bottom is placed into bore holes from 100 to 400 feet deep
2、水平埋管地源热泵Horizontal Closed-Loop
管道阵列安装在沟槽中，切割深度为3到5英尺，长度达数百英尺。 A piping array is installed in trenches cut 3 to 5 feet deep and hundreds of feet in length
3、地表水源热泵Surface Water Closed-Loop
管道阵列被淹没在池塘或湖泊中，至少8英尺深 A piping array is submerged in a pond or lake at least 8 feet deep
4、地下水源热泵Ground Water Open-Loop
井水从地下含水层通过地热泵抽水，然后返回含水层或排放到地表。在此处键入公式。 Well water from an underground aquifer is pumped through the geothermal heat pump and then returned to the aquifer or discharged to the surface
## 参考文献